## Slide 1: WORKFLOW AUTOMATION
WE REDIFINE SOLUTIONS.

## Slide 2: GRAPHITE LUBRICATION SYSTEM
A STEP TOWARDS GREENER ENVIRONMENT

## Slide 3: BRIEF DESCRIPTION
Graphite lubrication is a liquid based system used in the forging industry. The closed circuit graphite lubrication system reduces friction and forging loads, and improves die life.
WFA's lubrication system has a collection tank which is placed beneath the forging press where all the sprayed graphite lubricants are collected and transferred to the supply tank.
The system has proved to be a safe and eco-friendly alternative of dry graphite spray lubrication technique.

## Slide 4: GRAPHITE LUBRICATION PROCESS
Dry graphite spraying method is replaced with liquid graphite for lubrication in forging.
Graphite lubricant is flooded on the forging die.
Used graphite liquid is collected through a hopper in SS Collecting tank.
To restrict the bonding of graphite inside the tank, a stirrer is used to keep the mixture uniform and un coagulated.
To remove any foreign material mixed in liquid after forging, The liquid is passed through the magnetic separator before entering the SS Supply tank.
The liquid is filtered by primary and secondary filter, before it is flooded on the die.

## Slide 5
Safe workplace
Direct Human exposure to graphite molecules is eliminated.
No graphite deposits results in safe and non-slippery environment.
Leaner process
Lubrication can be simultaneously incorporated with main forging process.
Cycle time is reduced significantly.
Cost Reduction
Graphite infused in the liquid can be reused for multiple cycles, thus drastically reduces consumption of new graphite material.
WHY WE NEED GRAPHITE LUBRICATION SYSTEM?

## Slide 6
Automatic lubrication reduces production time and increases capacity of the industry.
Since the lubrication is installed along with the press the time required for lubrication can be completely eradicated.
Unlike the graphite spraying method there was no black graphite deposits found on the work floor.
HOW GRAPHITE LUBRICATION SYSTEM CHANGED FORGING INDUSTRIES

## Slide 7: SCHEMATIC REPRESENTATION
SS Supply Tank
Stirrer
Primary and secondary Filter
Magnetic Separator
SS Collection Tank
Forging Press
Press Control Unit
Pump
Hopper
Nozzle
Pump
Ground level

## Slide 8: COMPLETELY ASSEMBLED MACHINE

## Slide 9: PARTS OF SUPPLY TANK

## Slide 10: PARTS OF COLLECTION TANK

## Slide 11: THANK YOU!
www.workflowautomation.in
+91 9381053100 / +91 9940012107
office@workflowautomation.in